Diagnostic Interface For Optical Transceivers
20 min presentation for coming experts
Bernt fiber course
Robert Olsson/2009

---
- Specification for Optical Diag from GBIC, SFP
- Also referenced XFP and SFP+ (mandatory)
- In SFP it's optional
- Not supported in all interface cards
- Not supported by all SFP's

---
ethtool -D eth5
PHY Diagnostics for eth5:
Externally-Calibrated:
Average RX-Power:
Wavelength: 1310 nm
Temp: 53.6 C
Vcc: 3.33 V
TX-PWR: -21.2 dB ( 0.26 mW)
TX-BIAS: 15.9 mA
RX-PWR: -9.9 dB ( 0.41 mW)

---
- I2C bus on Optical Module
  - Two 256 byte pages
    - 0xA0 Interface ID
    - 0xA2 Diagnostic Interface For Optical Transceivers
I”C

---
- I2C bus on Optical Module
  Lot's of optional and vendor specific data
  Opt Alarm
  Opt Warnings
  - Complicated calibration.
    - Internal
    - External (need float)
I”C

---
- RX and TX range
  - 0 – 6.5535 mW
  - -40 – + 8.2 dBm (1 mW reference)

---
Update for bifrost workshop
2010-01-27
- Now works for SFP+ w. ixge driver
- Patches sent for linux kernel inclusion
  - Status: Not yet included

---
Update for bifrost workshop
2010-01-27
Questions?