Open Source Router @ 10g
Talk at KTH/Kista 2007-04-29
Robert Olsson/Uppsala University
Olof Hagsand/KTH

---
Open Source Router @ 10g
Motivation
Breakthrough
Multi core CPU
Buses
NIC	with multiple queue's
Operating systems
prime time for
Commercial interest
www.vyatta.com

---
Open Source Router @ 10g
Team
Bengt Görden/KTH
Olof Hagsand/KTH
Robert Olsson/Uppsala University
Challenges
Packet budget, bandwidth to reach 10g
PCIe (PCI-Express)

---
Open Source Router @ 10g
Hardware selection (More later)
Several vendors have boards
We tested some boards.
Good connections to Intel who
testing
 Neterion (s2io) has boards
SUN's has new interesting boards.

---
Open Source Router @ 10g
Software selection
Linux/bifrost
tuning for ip-forwarding
device drivers are crucial

---
Open Source Router @ 10g
Lab work. Setup etc.

---
Currently Intel NIC's

---
Not or were blessed...

---
Flexible netlab at Uppsala University
El cheapo-- High customable -- We write code :-)
Ethernet
|
|
Ethernet
Tested
device
sink
device
linux
Test generator
linux
* Raw packet performance
* TCP
* Timing
* Variants

---
Lab

---
High-end Hardware
Bifrost components 2008-01-03
=============================
This represents equipment which have "passed" our tests at some point of time.
NOTE. This implies no guarantee whatsoever.
Hi-End Opteron system:
TYAN Thunder n5550W (S2915-E) 1 *
256 MB Reg ECC PC3200 (400 MHz) 4 *
Opteron dual core 2222 processor 2 *
4U Chassi 1 *
USB memory stick 1 *
Option:
Redundant power supply
 EMACS MRG-6500P Redundant PSU 2x500W
Intel Corporation 82571EB GIGE based Network cards

---
HW in use @ UpUnet-S

---
Theoretical pps (packet per second) numbers to reach
 wire speed at 10 Gbit/s

---
TX performance with 1500 byte pkts Sending on 4 interfaces
simultaneously. We reach 25.8 Gbit/s. Theoretical 4*10 Gbit/s
Distribution is fair and we reach 25.8 Gbit/s...
Exercise bus, bandwidth etc.

---
TX performance with 64 byte pkts Sending on 4 interfaces
simultaneously. We reach 10 Mpps . (Packets Per Second)
Distribution is fair and we reach about 10 Mpps
in total. Exercise for latency etc.

---
Routing performance using one CPU
vs Theoretical numbers to reach wire speed at 10 Gbit/s
Single flow. No modules. IN 1-PORT -> OUT 2-Port

---
Routing performance using one CPU
vs Theoretical numbers to reach wire speed at 10 Gbit/s
Single flow. No modules. IN 2-PORT -> OUT dummy0

---
Routing performance using one CPU
vs Theoretical numbers to reach wire speed at 10 Gbit/s
Single flow. No modules. IN 2-PORT -> OUT 2-PORT (Same NIC)

---
Routing performance using one CPU
vs Theoretical numbers to reach wire speed at 10 Gbit/s
Single flow. Netfilter modules. IN 2-PORT -> OUT 2-PORT (Same NIC)

---
Routing performance comparison using one CPU
different bus setups and modules
Non-multiqueue driver. Packet budget approx 900 kpps using one CPU
So we route close to 10g wire speed with large packet sizes.

---
Routing performance comparison using one CPU
flow load (forcing hash and fib lookups) and
input 64, 512, 1500 bytes according to graph
Non-multiqueue driver.

---
What is the Multi-queue stuff?
Part of virtualization
Ability to share load among different CPU's
Ability classify and control network load at very high speed
Opens many new possibilities
Needs hardware support by Interface boards/chips
Needs software support by Operating System

---
Routing performance comparison using one CPU
flow load (forcing hash and fib lookups) and
pktsize 64, 512, 1500 bytes
MultiQ vs no MultiQ 2048@30 with 64 byte. Pkts
Less performance with 4 CPU's!!

---
Routing performance comparison using one CPU
flow load (forcing hash and fib lookups) and
pktsize 64, 512, 1500 bytes
All very exciting we run per-CPU parallel until we hit
TX. dev_queue_xmit, __qdisc_run
Virtual TX is needed
More and exciting work needed.... ;)

---
Open Source Router @ 10g
Questions Please....

---
A new network symbol has been seen...
The Penguin Has Landed