Open-source routing at 10Gb/s
Olof Hagsand (KTH)
Robert Olsson (Uppsala U)
Bengt Görden (KTH)
SNCNW May 2009
Project grants: Internetstiftelsen (IIS)
Equipment: Intel, SUN, AMD
Networks: UU and KTH

---
Introduction
Investigate packet forwarding performance of new PC hardware:
  - Multi-core CPUs
  - Multiple PCI-e buses
  - 10G NICs
  - Multi-queue classification
Can we obtain enough performance to use open-source routing in the 10Gb/s realm?

---
Measuring throughput
Packet per second
  - Per-packet costs
  - CPU processing, I/O and memory latency, clock frequency
Bandwidth
  - Per-byte costs
  - Bandwidth limitations of bus and memory

---
Measuring throughput
drops
breakpoint
capacity
overload
overload

---
Block hw structure example

---
Equipment summary
Hardware needs to be carefully selected
BifrostLinux 6.0 on kernel 2.6.29rc2 with LC-trie forwarding and NUMA support
Packet generator: modified pktgen, IXIA for reference
TYAN Thunder 2927 motherboard, NUMA, Hypertransport
Two Quad-core 2.6GHz AMD Opteron 2382
Single PCIe internal bus
10GE network interface cards with hardware hash-based classifiers
  1. Intel 82598 ixgbe. 10Gb/s XF SR dual port x8 PCIe server adapter.
  1. Sun niu. Sun Neptune dual 10Gb/s x8 PCIe network card with XFPs and TCAM classifiers

---
Hardware – Box

---
Hardware - NICs
Intel 10g board Chipset 82598
Sun Neptun niu 10g

---
Forwarding experiments
Throughput versus packet length
Throughput versus number of CPU cores
Throughput versus functionality
Test Generator
Tested device
Sink device
Main setup
Tested device
Reference setup
IXIA

---
Throughput vs packet length - bw

---
Throughput vs packet length - pps

---
Introducing realistic traffic
For the rest of the experiments we introduce a more realistic traffic scenario
Multiple packet sizes
  - Simple model based on realistic packet distribution data
Multiple flows (multiple dst IP:s)
  - This is also necessary for multi-core experiments since NIC classification is made using hash algorithm on packet headers

---
Packet size distribution (cdf)

---
Flow distribution
Flows have size and duration distributions
8000 simultaneous flows
Each flow 30 packets long
31000 new flows per second
  - Measured by dst cache misses observed at UU
Destinations spread randomly over 11.0.0.0/8
FIB contains ~ 280K entries
  - 64K entries in 11.0.0.0/8

---
Throughput vs # CPU cores - bw

---
Throughput vs # CPU cores - pps

---
Throughput vs Functionality
1. Small routing table, no modules
2. Netfilter module
3. Netfilter module and connection tracking
4. Netfilter module and full BGP routing table (280K routes)

---
Full-duplex preliminary measurements
Deflect output traffic to avoid contention at sender
Box with double PCIe bus architecture
Same traffic mix but expanded with 12.0.0.0/8 prefixes in other direction
Preliminary results show (two directions):
  - BW: 7518+8442Kb/s ~15.9Gb/s
  - PPS: 1147+1208Kp/s ~ 2.36 Mp/s
Test Generator
Tested device
Test Generator

---
Conclusions
Using hardware classifiers for multi-core CPUs is now possible with open-source routers
  - Close to 10 Gbp/s for realistic traffic distributions.
Need to close the ”gap” (last 5-10%)
More work on traffic classifiers, eg TCAMs, required
Full duplex shows > 15Gb/s results.